## Slide 1: Summary: All Exercises
http://163.25.101.87

## Slide 2: The Textbook
Computer Organization and Design: The Hardware/Software Interface. David A. Patterson and John L. Hennessy, Morgan Kaufmann Ed., Fourth Edition, 2004.

## Slide 3: Reminds
80 pts of problems in the exam will be similar (but not the same) problems in the exercise!

## Slide 4: How to turn in the exercises
Hand-written paper works!
Turn in the exercises by the next Tuesday (2012/07/24)
Send to my mail box in the department office
No Meeting at the next Tuesday!

## Slide 5: Exercise 1
Translate the following C program to MIPS/ARM assembly code
int i, A[100], B[100], S;
S = 0;
for (i=0;i<100;i++)
S = S + A[i]*B[i];

## Slide 6: Exercise 2
You are writing a program on an embedded processor without hardware multiplier/dividor.
Write a C program to do multiplication over two 8-bit unsigned integers
  Assume: the register is of 16-bit width
  You can only use the following operators: +, -, ~, &, |, ^, <<, >>, <, >, ==, >=, <=, !=

## Slide 7: Exercise 3
Explain each of the following hazards
  Data hazard
  Control hazard
  Structural hazard
For each type of these hazards, give an example code to explain where the pipeline stall (bubble) occurs

## Slide 8: Exercise 4
Consider the MIPS pipeline
Design the digital circuit to detect the data hazard between two consecutive instructions
  Generate a signal STALL=1 if data hazard occurs

## Slide 9: Exercise 5
Consider a 32KByte 2-way set associative cache
Write down the 32-bit address format to access the cache
Format of your answer:
tag
index
offset
??? bits
??? bits
??? bits
Note: the cache parameters will be changed

## Slide 10: Exercise 6
Modify the MIPS pipeline for the following changes on load/store instructions
  a load/store instruction has no displacement now
    LD R2, R3 //R2=mem[R3]
  additional LDI/STI instruction for load/store with address increment
    LDI R2, R3 //R2=mem[R3]; R3=R3+1

## Slide 11: Exercise 6 (cont’d)
Your answer should include
  the pipeline data path
  control scheme for data forwarding
  control scheme to stall the pipeline due to data hazard
Format to express the control scheme:
  rules to check for hazard from pipeline registers
if (EX/MEM.Regwrite
and EX/MEM.RegisterRd=ID/EX.RegisterRS) ForwardA=10