## Slide 1: Mid-Term Project (Lab)
multi-function stop-watch

## Slide 2: Your Task: Design a stopwatch
start timer counting when “start” button pressed
stop timer counting when “stop” button pressed
reset time to zero when “reset” button pressed
(Figure 7-23, Section 7-10)

## Slide 3: Purpose of the lab
to learn the RTL design methodology (Section 7-2)
the digital clock in Lab 05
Learn how to control the counting

## Slide 4: Grading Policy
Basic: 60%
  time refresh every 0.01 second (needs modification to digital clock)
  carry: 00.99 -> 01.00, 59.99 -> 00.00
Option 1: control the counting by buttons (+10%)
  Implement start/stop/reset buttons
Option 2: CSS (compare-and-store) (+10%)
  additional button CSS
  compare and store the maximum value in an internal register
  press another button B to recall the maximum value
Option 3: make the time display blink (+10%)
  After pressing another button C
Report: 10%

## Slide 5: Pre-Lab Report
(1) your paper design (power-point/word/latex/Quartus II) of this lab
  data path
  control unit:
    finite state machine
    the circuit
(2) expected timing waveform for each sub-module of your design
  list typical working cases for each sub-module
  in power point/word/latex
(3) timing waveform for each sub-module of your design
  Quartus II simulation
Remark: modular design required!
  no more than (3/2)2 times the screen size when you can see every word clearly