## Slide 1: Midterm Problems and Solutions
Covers Chap. 5 & 7

## Slide 2: Coverage of your midterm exam
be familiar with the two design techniques:
  sequential circuit design from the general framework (Chap. 5, Sec. 7.1, Sec. 7.6)
  RTL design (Sec. 7.2 – 7.4)
clock

## Slide 3: General procedure to design a sequential circuit
Step 1: draw the state diagram and state table
Step 2: assign state values and flip flops
Step 3: draw the spec of the combinational part
  draw the truth table
Step 4: realize the combinational part
  logic simplification if necessary
clock

## Slide 4: Steps of RTL Design
Step 1: always starts from the general framework
  control signals: the order sent from control unit
  status signals: reports from data path
Step 2: specify the behavior of each part
  control unit: state-diagram
  data path: micro-operation
Step 3: design circuits from behavior specification
  control unit: state-diagram to circuit (Chapter 5)
  data path: micro-operation to circuit (Sec. 7.3 – 7.6)

## Slide 5: General Rules of the Exam
Open Book (but no discussion)
You can use any circuit mentioned in the textbook as a building block (without drawing detailed gate-level circuit)
  unless special restrictions are imposed
Just specify the Boolean equation for a combinational circuit

## Slide 6: Problems (Part 1)
Standard exercises

## Slide 7: Problem 1
Timing analysis for an sequential circuit

## Slide 8: Problem 1
Draw the timing waveform for the following circuit

## Slide 9: Problem 1
Draw the timing waveform for the following circuit
clk
time
X
Y
00
0
1
1
1
0
0
0
0
0
0
???

## Slide 10: Solution to Problem 2
clk
time
X
Y
00
0
1
1
1
00
10
0
0
01
0
0
01
0
0

## Slide 11: Problem 2
Circuit design from a state diagram

## Slide 12: Problem 2
Draw the circuit to realize the state diagram
00
01
10
X=1
X=0
X=0 or X=1
X=0
X=1

## Slide 13: Solution to Problem 2
Combinational
Circuit
D
D
X
S1
S0
D1
D0

## Slide 14: Problem 3
Up-down counter with parallel load

## Slide 15: Problem 3
Depict a gate-level design of a 4-bit down counter with parallel load
  in AND/OR/NOT gates and MUXs
  explain how you devise the circuit
counter
clock
4
D
4
Q
Load
Count
Load(t)
Count(t)
Q(t+1)
0
0
Q(t+1)=Q(t)
0
1
Q(t+1)=Q(t)-1
1
X
Q(t+1)=D(t)

## Slide 16: How to design a down counter
Observation: when Qi will be inversed (the design strategy)
Redraw the circuit framework (to inverse Qi)
Derive Boolean equation to inverse Qi
Circuit simplification
0110
0101
0100
0011
0010
0001
inverse Q2 since Q1=0 and Q0=0
(when EN=1)
inverse Q1 since Q0=0

## Slide 17: How to design a down counter
Observation: when Qi will be inversed (the design strategy)
Redraw the circuit framework (to inverse Qi)
Derive Boolean equation to inverse Qi
Circuit simplification
0 0 0
0 1 1
0 1
1 1 0
combinational
circuit

## Slide 18: How to design a down counter
Observation: when Qi will be inversed (the design strategy)
Redraw the circuit framework (to inverse Qi)
Derive Boolean equation to inverse Qi
Circuit simplification
combinational
circuit

## Slide 19: Solution
draw the circuit framework for multiple functions
complete the part for counting
the complete circuit
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q-1)
Count
Load

## Slide 20: Solution
draw the circuit framework for multiple functions
complete the part for counting
the complete circuit
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q-1)
Count
Load=1
Load(t)
Count(t)
Q(t+1)
0
0
Q(t+1)=Q(t)
0
1
Q(t+1)=Q(t)-1
1
X
Q(t+1)=D(t)

## Slide 21: Solution
draw the circuit framework for multiple functions
complete the part for counting
the complete circuit
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q-1)
Count
Load=0
Load(t)
Count(t)
Q(t+1)
0
0
Q(t+1)=Q(t)
0
1
Q(t+1)=Q(t)+1
1
X
Q(t+1)=D(t)

## Slide 22: Solution
draw the circuit framework for multiple functions
complete the part for counting
the complete circuit
D
D
D
D
MUX
MUX
MUX
MUX
combinational
circuit
(A=Q-1)
Count
Load
How to design?

## Slide 23: Recall: the down-counter design
combinational
circuit

## Slide 24: The complete design
combinational
circuit

## Slide 25: Problem 4
Timer

## Slide 26: Problem 4: Timer
start counting down when “START” button pressed
  00:00 -> 00:01 -> … -> 00:99 -> 01:00 ->01:01 -> …->59:99 -> 00:00
  refresh every 0.1 second
  Receive 1 KHz clock signal
(a) Circuit to generate 1-cycle pulse every one second
(b) 4-digit counter of the timer
timer
1 KHz clock
4
EN
8
display
0.01 second
second
Start
Stop
Reset
(Hint: use RTL design method)

## Slide 27: Circuit to generate 1-cycle pulse
Divide-by-ten clock generator
BCD
Counter
Q
Q==9
CO
counter
CO
0
1
1
2
3
4
…
0
8
9
0
time
0
10 cycles = 0.01 second

## Slide 28: 4-digit counter
BCD
Counter
CO
EN
Q
BCD
Counter
CO
EN
Q
ms0
ms1
BCD
Counter
CO
EN
Q
Mod-6
Counter
CO
EN
Q
S0
S1
From div-10 circuit

## Slide 29: Problem 5
Realizing arithmetic operations with RTL design

## Slide 30: Problem 5
Design the circuit to realize the computation
  Q = (A-B) + (C-D)
Write-down:
  State diagram of the control unit
  Circuit of the data path
Your
Design
n
A
n
B
n
C
n
D
START
n
Q
FINISH

## Slide 31: The hardware algorithm
STOP
Step 0
Step 1
Step 2

## Slide 32: The data path
Capable of realizing all operations in the algorithm
STOP
Step 0
Step 1
Step 2
Adder
MUX
~B
C
~D
MUX
A
register Q
Load
SELB
L
SELA
Cin
0
1
00
01
10

## Slide 33: State diagram for the control unit
Control signals (L, SELA, SELB, Cin)
STOP
Step 0
Step 1
Step 2
(0, X, XX, X)
(1, 1, 00, 1)
(1, 0, 01, 0)
(1, 0, 10, 1)
Adder
MUX
~B
C
~D
MUX
A
register Q
Load
SELB
L
SELA
Cin
0
1
00
01
10

## Slide 34: Problems (Part 2)
Creative Exercises

## Slide 35: Problem 6: Minimize Amount of Registers in a Circuit (20%)
Design the data path to realize the following computation
  C=A+B
  D=E+F
  A=C-D
  D=D+A
  output the content of D
use minimum amount of registers to store values A-F
  each of A, B, C, D, E, F not necessary has a dedicated register
Write-down:
  micro-operations with control signals specified
  circuit of the data path
  how you minimize amount of registers
the computation may
be changed

## Slide 36: Problem 7: Greatest Common Divisor (25%)
Find the greatest common divisor (最大公因數) for two integers A and B
  Hardware algorithm
  State-diagram of the control unit
  Circuit diagram of the data path
GCD
start
n
B
n
Q
n
A
Finish